## Slide 1
Robotic Control: A Case Study on Self-Balancing Systems
Arelia McKern | Magdalena Janocha
Supervisor: Prof. Geimer
Project Leader: Bobo Helian

## Slide 2: Why Self-Balancing Robots are a Control Benchmark
Self-balancing robots are inherently open-loop unstable
Small disturbances, sensor noise or delays immediately affect stability
Successful control requires fast, closed-loop feedback and robust tuning
This makes the system an ideal benchmark for → real-time control → sensor integration → simulation-to-hardware transfer
Project Goal: Stabilize the robot and extend balance to functional behavior
Notes: Self-balancing robots are a paradox: They are mechanically simple — yet dynamically highly unstable.
A deviation of a few degrees is enough to make the system fail. This makes them an ideal benchmark for real-time control, sensor fusion and robust closed-loop design.

## Slide 3: Hardware – Sensor tests
IR-Sensor (Line Sensor) Ultrasonic Sensor
Notes: First – tested Sensors: For path and navigation really important IR Sensor (Line Sensor):
Sensor response analyzed with respect to distance to the ground
Optimal operating height identified at approximately 10 mm
Mechanical shielding added → reduced influence of ambient light and external light sources
Black paper moved underneath the sensor to simulate a path
Clear distinction between light and dark surfaces achieved
Ultrasonic Sensor:
Measurements performed along a known, measured distance
Tests with a moving object to simulate obstacles
Evaluation of signal dynamics, noise and measurement behavior
Basis for collision detection and obstacle avoidance
Sensor characterization provides reliable inputs for subsequent control tasks

## Slide 4: Hardware
Mounting bracket for TCRT 5000 (Rapid Prototyping with LEGO)
Notes: Rapid prototyping approach using LEGO mounting brackets
Allowed fast iteration and flexible adjustment of sensor position and height
Prototype 1: Sensor between the wheels / inside the track
Pros:
  Sensor closely aligned with robot center of mass
  Less influence from steering motions
  Compact and mechanically protected
Cons:
  Limited field of view
  Short reaction time at higher speeds
  Less suitable for anticipating sharp curves
Prototype 2: Sensor mounted further forward
Pros:
  Earlier detection of the line
  Better anticipation of curves and path changes
  Smoother trajectory tracking possible
Cons:
  Higher sensitivity to vibrations
  Stronger influence of pitch motion
  More exposed to collisions and uneven ground
  ---> outside of the line because of the distance of 0.5cm Lego

## Slide 5: Hardware
Notes: A0 A1 belegt
A6, A7 wären frei, sind halt aber nicht erreichbar, deswegen IR neben Ultraschall weg

## Slide 6: Hardware - Outlook
Notes: Beide Sensoren auf Kante
Einer drauf, der andere Daneben

## Slide 7: Simulation demo
Video von Yaw
Reglerstrukur

## Slide 8: Simulation Outlook

## Slide 9: Task 1
Notes: Zeitsteuerung beim Obstacle, blaue LEDS zeigen Detektion
Regler bisher einfach cases

## Slide 10: Task 2
Notes: Erkennen das ende der linie nicht, wird geschaut, wann wird das letze mal schwarz gesehen haben, wenn zu lange her, dann blaue leds und encoder blaue LEDs

## Slide 11
Thank your for your attention!

## Slide 12
Backup